## Slide 1
Groundwater Quantity Indicators for Oil Sands Monitoring
May, 2023
Documentation for Submission of Deliverables:
Data Availability
Digital Data Set
By: Jordan Brinsky, Brent Welsh, Dan Palombi

## Slide 2: Neogene - Quaternary Water Level Data Sources
    Multiple data sources that contained water levels from Neogene-Quaternary aged sediments were compiled. A description of each source is provided below. Additional details on how the data was initially processed and allocated is described in the following slides.
    Advisian
      Data mined by Advisian from Environmental Impact Assessments and EPEA Groundwater Monitoring Reports; Received from Innotech as Table 1 (Well Details) and Table 2 (Water Levels)
COSIA
      Data used by Matrix to calibrate the SAOS groundwater model in 2016. This dataset primarily consists of groundwater levels from Mannville aquifers but also includes some water levels from Neogene-Quaternary aquifers. Received from InnoTech as two tables; one with well details the other with water levels
    Groundwater Observation Well Network (GOWN)
      Water level data mined by the AGS from the GOWN website
    Alberta Water Well Information Database (AWWID)
        Static water levels from water well drillers' reports mined from the AWWID by AGS
        Water Use Reporting System (WURS)
          Additional data received from AEPA that contains water levels from Water Act licence requirements

## Slide 3
Utting, (In Press) – NAOS Geobodies and Quaternary Unit Picks
Recently completed maps characterizing the shallow subsurface in the NAOS and SAOS areas were used to help differentiate wells completed in Neogene-Quaternary sediments. Top elevations and areal extents are shown in slides 3-10. Modelled Geobodies (ascii format) and Unit Picks (tabular form) for 12 geobodies in the NAOS region were mapped. This work was used to allocate monitoring wells and source wells to zones within the Neogene-Quaternary.
(Steepbank Intermediate Sand)

## Slide 4
Utting, In Press – NAOS Geobodies and Quaternary Unit Picks
3

## Slide 5
Utting, In Press – NAOS Geobodies and Quaternary Unit Picks

## Slide 6
Utting, 2021 SAOS Geobodies - Empress
Modelled Geobodies (ascii format) and Unit Picks (tabular form) for 17 geobodies in the SAOS region were mapped in (Utting, 2021) (https://ags.aer.ca/publication/dig-2021-0017) and used to allocate the Quaternary data. An update in naming convention for these geobodies and the distinction of the Bonnyville geobody into the Bonnyville Sand and Bonnyville Unit 1 and Bonnyville Unit 2 have recently been completed (Utting, In Press). A summary of the nomenclature changes between Utting, 2021 and Utting (In Press.) is provided in Slide 11)

## Slide 7
Utting, 2021 SAOS Geobodies - Empress

## Slide 8
Utting, 2021 SAOS Geobodies - Ethel

## Slide 9
Utting, 2021 SAOS Geobodies - Muriel

## Slide 10
Utting, 2021 SAOS Geobodies – Bronson and Bonnyville

## Slide 11
Summary of the nomenclature changes in Utting (In Press) and Hartman (In Press)
Empress Unit 1  House member Ipiatik Formation
Empress Unit 2  Wappau member Ipiatik Formation
Empress Unit 3  Calder member Ipiatik Formation
Empress Terrace  Winefred Formation of the Empress Group
Utting, In Press – New Neogene-Quaternary Nomenclature

## Slide 12
Advisian Data Allocated to Geobodies in the NAOS Region
AGS received two excel tables from Innotech of data compiled through a data mining exercise conducted by Advisian:
Table 1 (Containing well information)
Table 2 (Water Level Information)
Some of the data had a formation name already allocated to it in Table 1, which is based on either;
  The screened lithology,
  The name of the well,
  Formation name reported in the EIA
Well information included two surface elevations
Ground surface elevation,
Datum elevation,
To allocate the data to geobodies, completion elevations were required. Most of the well details contained completion depths, which needed to be converted to elevations for allocation. Wells with geographical coordinates were brought into Arc and sampled to a 2m bare earth LiDAR grid. This LiDAR elevation was used to calculate completion elevations where necessary. Where available, the elevation that was used to calculate a completion interval for allocation was as follows (in order):
  Datum elevation
  Ground surface elevation
  LiDAR elevation
Wells had columns for completion intervals (listed as depths), that were used to calculate the completion interval in the following order:
  Screen depths,
  Sandpack depths, or
  Well Bottom depths

## Slide 13
Advisian Data Summary
The allocation reported in Table 1, which was mined from EIAs and reports was used to determine if a well was completed in a Neogene-Quaternary aged aquifer.
Table 1 consisted of 2760 well IDs
1687 well IDs had geographical coordinates
871 of these wells had a 'Neogene-Quaternary' unit reported as the formation they were completed in
  829 of these had water levels reported in Table 2
An additional 296 wells had “Unknown” reported for the formation they were completed in
  35 of the 296 wells had water levels reported in Table 2
  4 of the 35 were in Neogene-Quaternary aquifers based on allocation with the Bedrock topography map of Alberta.
  12 of the 35 did not have depths and were not able to be allocated
  The remaining 19 were in the bedrock according to the Bedrock topography map of Alberta
These wells were differentiated further by using the modelled geobodies from Utting (In Press) and Utting, 2021
The well details from Table 1 is attached as: advisian_table_1.xlsx

## Slide 14
Advisian Data Allocated to Geobodies with Water Levels
Monitoring wells potentially located in the undifferentiated Neogene-Quaternary
Monitoring wells allocated to modelled geobodies from Utting (In Press)

## Slide 15
The AGS received two tables of COSIA monitoring wells from InnoTech (originally compiled by Matrix) consisting primarily of water levels from Mannville Aquifers
In addition to data from the Mannville Aquifers, there were 17 wells completed in surficial aquifers.
This data was from 14 monitoring wells and 3 source wells.
The oldest water levels were from 1998, while the most current water levels were from 2011.
The location and details of the COSIA wells is attached as: cosia.xlsx
COSIA DATA

## Slide 16
Neogene - Quaternary GOWN Wells
Initial scoping found 54 potential GOWN wells completed in surficial aquifers
Status Reported | Count
Inactive | 6
Active WL & WQ | 41
Metadata Only | 5
Inactive WQ only | 1
Active WL only | 1
The 54 GOWN wells had the status reported and aquifer reported as follows:
Aquifer Reported | Count
Quaternary | 1
Empress Channel | 3
Sand River | 4
Ethel Lake | 5
water table | 4
Bonnyville Sand | 6
Birch Channel | 4
Surficial | 11
Surficial Sands | 3
Muriel Lake | 1
Empress | 1
Grand Centre | 1
Empress Terrace | 3
Bonnyville | 3
Sand River (Bonnyville Unit 2) | 1
Bonnyville Unit 2 | 2
Quaternary Group | 1
Information on the location and well details of GOWN wells monitoring Neogene – Quaternary is attached in the accompanying spreadsheet: gown.xlsx

## Slide 17
AWWID DATA – Distinguishing between Bedrock and Neogene-Quaternary wells.
Water wells from the AWWID with static water levels were gathered and clipped to the area of the Athabasca Oil Sands
Wells were sampled to 2m LiDAR to give an estimate of the ground surface where available. For wells in areas without 2 m LiDAR, the 15m LiDAR was used
If the well had completion depths reported, the upper and lower elevation was calculated using the LiDAR elevation
If no completion depth was reported the total depth of the well was used.
The data was allocated using a machine-learning method, that looked at lithological descriptions. If no lithological descriptions were available the well was allocated to The Bedrock Topography of Alberta Version
  https://ags.aer.ca/data-maps-models/maps/map-610

## Slide 18
AWWID DATA – Allocating Neogene-Quaternary Data
Wells were allocated to Geobodies in both the NAOS and SAOS regions using the recently completed NAOS geobodies and modelled unit picks; as well as modelled geobodies in the SAOS region from Utting, 2021
  https://ags.aer.ca/publication/dig-2021-0017
126 water levels from 116 water wells were allocated to surficial Geobodies
Geobody | Count
Alder Channel | 3
Birch Channel | 9
Bonnyville | 26
Bronson | 12
Empress Central | 4
Empress Christina | 1
Empress Unit 1 | 11
Empress Unit 2 | 1
Empress Unit 3 | 1
Ethel Christina | 14
Ethel Leismer | 3
Ethel Sunday Creek | 4
Muriel | 9
Muskeg Mountain Till 1 | 7
Muskeg Mountain Till 2 | 4
Muskeg Mountain Till 3 | 3
Muskeg Mountain Till 4 | 10
Muskeg Mountain Till 5 | 2
Steepbank Clay | 1
Steepbank Mid Sand (intermediate sand) | 1

## Slide 19
AWWID DATA – Allocating Neogene-Quaternary Data
The remaining wells (1970 water levels from 1886 water wells) were assigned as undifferentiated Surficial Wells
Water levels from the AWWID database are provided in the accompanying spreadsheet awwid.xlsx

## Slide 20
WURS DATA – Allocating Neogene-Quaternary Data
WURS data was allocated using the formation provided on water licenses
Water levels were found for 360 wells in the AOS area
Source | Count
Undifferentiated-Surficial | 196
Sand River Aquifer | 6
Muriel Lake Aquifer | 8
Marie Creek Aquitard | 8
Ethel Lake Aquifer | 37
Empress Terrace | 1
Empress Aquifer - Gregoire Channel | 4
Empress Aquifer - Christina Channel | 11
Empress Aquifer (Undifferentiated) | 58
Empress (Mackay Channel) | 1
Bronson Lake Aquitard | 1
Bonnyville Aquifer | 7
Birch Channel | 22
Wurs_wells.xslx

## Slide 21: Next Steps
Confirm allocation of data
  Try to determine if any of the undifferentiated Quaternary data are part of buried channel aquifers
  Include the newly mapped Bonnyville Unit
Data Request to Industry
  Water levels and Tops
QC data
    Flag AWWID data that are plotted at the centre of sections, LSDs or, Quarter Sections
    Confirm WURS well locations
Map Baseline hydraulic head for NAOS and SAOS regions